## Slide 1: NAVIO 2 드론 제작
2019년 6월 9일
성병문
한세대학교 자율 비행

## Slide 2: NAVIO 개요

## Slide 3: NAVIO2
홈페이지
  https://emlid.com/navio/
  https://docs.emlid.com/navio2/
What is NAVIO2?
  Autopilot HAT(Hardware Attached on Top) for Raspberry Pi
  Powered by ArduPilot and ROS
  Supports PX4
  $ 168
  Turn your Raspberry Pi® into a drone controller

## Slide 4: NAVIO2 특징
GNSS receiver
  Tracks GPS, GLONASS, Beidou, Galileo and SBAS satellites. External antenna with MCX connector
Dual IMU
  Accelerometers, gyroscopes and magnetometers for orientation and motion sensing
RC I/O co-processor
  Accepts PPM/SBUS input and provides 14 PWM output channels for motors and servos
High resolution barometer
  Senses altitude with 10 cm resolution
Extension ports
  Exposed ADC, I2C and UART interfaces for sensors and radios
Triple redundant power supply
  With overvoltage protection and power module port for voltage and current sensing

## Slide 5: NAVIO 운영체제 설치
This is a Raspbian you know with ArduPilot and ROS preinstalled and ready to run with a couple of simple commands. Also comes with DroneKit and GStreamer

## Slide 6: NAVIO H/W 조립
조립

## Slide 7: NAVIO2 드론 조립 예
https://community.emlid.com/t/first-build-quadcopter-autonomous-drone-rpi-3-b-navio2/12597
https://www.instructables.com/id/Step-by-step-Guidance-to-Build-a-Drone-From-Scratc/

## Slide 8: NAVIO2 조립
홈페이지
  https://docs.emlid.com/navio2/
Powering Navio2 Attention
  ALL POWER SOURCES SHOULD PROVIDE VOLTAGE IN 4.8-5.3V RANGE, OTHERWISE YOU CAN DAMAGE YOUR NAVIO2 AND RASPBERRY PI.**
Navio2 has three power sources, all of them can be used simultaneously as they are protected by ideal diodes.

## Slide 9: 나비오2 부품 설명

## Slide 10: NAVIO 쿼드콥터 배선 ½

## Slide 11: Navio2 쿼드콥터 배선 2/2

## Slide 12: Navio2 고정익 배선 ½

## Slide 13: Navio2 고정익 배선 2/2

## Slide 14: Navio2 로버 배선 ½

## Slide 15: Navio2 로버 배선 ½

## Slide 16: Navio2 로버 배선 2/2

## Slide 17: 파워 공급 1
Navio2 should be powered by a power module connected to the “POWER” port on Navio2.
Navio2 will provide power to the Raspberry Pi.

## Slide 18: 파워 공급 2

## Slide 19: GPS 연결

## Slide 20: ESC 연결
ESCs are connected to RC outputs labeled from 1 to 14 on a 2.54mm header.
Only one ESC power wire (central) should be connected to Navio2 servo rail, otherwise BECs built in ESCs will heat each other.

## Slide 21: 고도계 태양광/바람 차단(필수)
MS5611 barometer (steel cap IC) is sensitive to UV light and might report sudden jumps in altitude under sunlight.
It is very important to cover it with a piece of open cell foam (something like microphone fabric) or put autopilot in a protective case to protect it both from sunlight and airstreams.

## Slide 22: RC input
Navio2는 PPM 과 SBUS 형식의 RC 신호만을 지원한다.
PPM 타입 RC Controller
  Frsky Taranis
    https://www.frsky-rc.com/product/taranis-x9d-plus-2/

## Slide 23: FrSKY X8R과 Navio2 연결 1

## Slide 24: FrSKY X8R과 Navio2 연결 2

## Slide 25: Futaba T18SZ와 R7008SB 연결

## Slide 26: Telemetry Modem
UART radio
  For UART port use /dev/ttyAMA0 serial.

## Slide 27: Telemetry Modem
3DR 무선 텔레 메트리 433MHZ
  https://www.banggood.com/ko/New-Upgraded-V2_0-3DR-Radio-Telemetry-433MHZ-915MHZ-Data-Transmission-Module-For-APM-Pixhawk-PX4-p-1304758.html?ID=510651&cur_warehouse=CN
  주파수 : 915MHZ, 433HZ (옵션)
  수신 감도 : -121 dBm
  송신 전력 : 20dBm(100mW)
  투명한 직렬 링크
  무선 전송 속도 최대 25kbps
  ranges of better than 300m
  the range can be extended to several kilometres
    with the use of a patch antenna on the ground).

## Slide 28: Telemetry 연결 예시

## Slide 29: 진동 방지 받침대 1
We have designed an anti-vibration for Navio that can be easily 3D printed.
It significantly simplifies mounting and eliminates vibrations.

## Slide 30: 진동 방지 받침대 2
STL Files
  Top
    https://github.com/emlid/hardware/blob/master/VibroNavio2top_rev_A.STL
  Bottom
    https://github.com/emlid/hardware/blob/master/VibroNavio2bot_rev_A.STL
You will also need 8 blue vibration damping balls from Hobbyking
  https://hobbyking.com/en_us/vibration-damping-ball-65g-bag-of-8.html

## Slide 31: 라즈베리파이 케이스
https://www.thingiverse.com/thing:3712499?fbclid=IwAR0q23hTFudF2WR6drXF0MihutdcCVjp1nGQSJyXfh7dTh9L-Sk7-IEVzkE
https://www.thingiverse.com/thing:3714695?fbclid=IwAR2kpwI0rKJyGNhlsDpJ_Qi9enSqlocVV1SZ8qa6bXuRHgcDlFpWOtUVXCo

## Slide 32: 고정익 만들기
블랙이글 스티로폼 비행기 만들기

## Slide 33: Navio2 고정익 배선 2

## Slide 34: Navio2 고정익 배선 3

## Slide 35: 서보 파워 공급 방법
Servos are connected to RC outputs labeled from 1 to 14 on a 2.54mm header.
Power module does not provide power to servos.
To provide power to servos connect BEC to the servo rail.
BEC would also serve as back-up power supply to Navio2.

## Slide 36: Wheel Position

## Slide 37: Servo Output Original Configuration

## Slide 38: Servo Output

## Slide 39: 날개 각도

## Slide 40: NAVIO S/W
라즈비안 운영체제 설정
ardupilot 설정

## Slide 41: 라즈비안 운영체제 설정
라즈비안 운영체제 설치
라즈비안 환경 설정(Wi-Fi)
ardupilot 설정

## Slide 42: 나비오 S/W 설치
공식 문서
  https://docs.emlid.com/navio2/

## Slide 43: 라즈비안 설치
기설정된 라즈비안 이미지 다운로드
  http://files.emlid.com/images/emlid-raspbian-20190227.img.xz
Etcher를 이용하여 라즈비안 이미지를 SD-Card에 굽는다.
  Etcher 다운로드 : https://www.balena.io/etcher/

## Slide 44: 라즈비안 Wi-Fi 설정
Wi-Fi 설정
  sudo vi /etc/wpa_supplicant/wpa_supplicant.conf
    network={
      ssid="ADRONE"
      psk="12341234"
    }
  sudo nano /etc/wpa_supplicant/wpa_supplicant.conf

## Slide 48: 라즈베리파이 IP 주소 알아내기
공유기에서 접속한 라즈베리파이의 아이피 주소를 알아낸다.

## Slide 49: 라즈베리파이 IP 주소 고정하기
공유기에서 접속한 라즈베리파이의 아이피 주소를 고정한다.

## Slide 50: 라즈베리파이 로그인
ssh 프로그램 다운로드
  bitvise ssh client 설치 :
    https://www.bitvise.com/download-area
라즈베리파이 로그인
  아이디: pi
  암호: raspberry

## Slide 51: 라즈베리파이 환경 설정 2
암호 변경 : 암호를 a 로 변경한다.
  pi 사용자의 암호 변경
    sudo passwd pi
  관리자 암호 변경
    sudo passwd
업데이트/업그레이드는 일주일에 한 번 한다.
  sudo emlidtool rcio update
  sudo apt update
  sudo apt upgrade –y
  sudo apt autoremove

## Slide 52: SD 카드 전체 용량 사용 설정
아래의 명령어로 SD 카드의 전체 용량을 사용하도록 설정한다.
  sudo raspi-config --expand-rootfs
  sudo reboot
SD 카드 사용 용량 확인 방법
  df -H
확인

## Slide 53: 라즈베리 나비오 운영체제 정보
커널 버전 확인
  uname -a
배포판 버전 확인
  lsb_release -a

## Slide 54: Ardupilot 설치 사전 체크 사항

## Slide 55: SD Card 성능 벤처 마크

## Slide 56: SD Card 성능 체크
성능 체크 방법
  curl https://raw.githubusercontent.com/geerlingguy/raspberry-pi-dramble/master/setup/benchmarks/microsd-benchmarks.sh | sudo bash
  curl http://www.nmacleod.com/public/sdbench.sh | sudo bash

## Slide 57: Sandisk 성능 체크 결과

## Slide 58: Sandisk 성능 체크 결과

## Slide 59: Ardupilot 설정

## Slide 60: Ardupilot 설정
공식 문서
  https://docs.emlid.com/navio2/common/ardupilot/installation-and-running/

## Slide 61: Choosing a vehicle, version and board
To select the vehicle that would be launched by default you should configure it with emlidtool:
  sudo emlidtool ardupilot
Before configuration emlidtool checks your RCIO firmware and will suggest to update it if you have the outdated one:

## Slide 62: Choose your vehicle
In the example below we'll use arducopter but it could've been just as well arduplane or ardurover.

## Slide 63: Choose copter and Apply

## Slide 64: Specifying launching options
Open the file:
  sudo nano /etc/default/arducopter
  sudo systemctl daemon-reload
Here you can specify IP of your ground station.
TELEM1="-A udp:127.0.0.1:14550"
TELEM2="-C /dev/ttyAMA0" # Options to pass to ArduPilot
ARDUPILOT_OPTS="$TELEM1 $TELEM2"
# -A is a console switch (usually this is a Wi-Fi link)
# -C is a telemetry switch
# Usually this is either /dev/ttyAMA0 - UART connector on your Navio
# or /dev/ttyUSB0 if you're using a serial to USB convertor
# -B or -E is used to specify non default GPS
접속 노트북의 IP 주소로 변경
텔레메트리 사용 설정

## Slide 65: 최신 Ardupilot 프로그램 설치(X)
나비오 설치 버전을 사용하거나
  cp /usr/bin/arducopter ~
최신 버전 다운로드 및 권한 부여
  wget --no-cache http://firmware.eu.ardupilot.org/Copter/stable/navio2/arducopter
  chmod +x arducopter

## Slide 66: Launching a custom ArduPilot binary 2
sudo nano /etc/systemd/system/ardupilot.service
[Unit]
Description=ArduPilot for Linux
After=systemd-modules-load.service
Documentation=https://docs.emlid.com/navio2/navio-ardupilot/installation-and-running/#autostarting-ardupilot-on-boot
Conflicts=arduplane.service arducopter.service ardurover.service
[Service]
EnvironmentFile=/etc/default/ardupilot
# Uncomment and modify this line if you want to launch your own binary
ExecStart=/bin/sh -c "/home/pi/arducopter -A udp:192.168.1.200:14550 -C /dev/ttyAMA0"
##### CAUTION ######
# There should be only one uncommented ExecStart in this file
Restart=on-failure
[Install]
WantedBy=multi-user.target
최신 ardupilot 프로그램 경로
접속 노트북의 IP 주소로 변경
Notes: sudo vi/etc/systemd/system/ardupilot.service

## Slide 67: Ardupilot 서비스 관리 3
ArduPilot 재시작
  sudo systemctl daemon-reload
  sudo systemctl status ardupilot
  sudo systemctl start ardupilot
  sudo systemctl enable ardupilot
라즈베리파이 리부팅
  sudo reboot
수동 실행 방법
  sudo arducopter -A udp:192.168.1.200:14550

## Slide 68: ardupilot 실행 확인 방법
아래의 명령어를 실행하여 ardupilot 실행 여부를 확인한다.
  ps -ef | grep ardu
비 정상 실행 상태 : 아이피 주소가 잘 못 됨.
정상 실행 상태 : 아이피 주소 확인

## Slide 69: Ardupilot 소스 빌드(X)
필수 사항 아님.

## Slide 70: 쿼드로터 arducopter 소스 빌드
Python 패키지 설치
  pip install future
Aliasing
  alias waf='/home/pi/ardupilot/modules/waf/waf-light'
Download the ArduPilot code and update submodules:
  git clone https://github.com/ArduPilot/ardupilot.git
  cd ardupilot
  git pull
  git submodule update --init --recursive
Waf config
  waf configure --board=navio2
Build arducopter
  waf copter
Copy the binary
  cp build/navio2/bin/arducopter ~

## Slide 71: 고정익 arduplane 소스 빌드
Python 패키지 설치
  pip install future
Aliasing
  alias waf='/home/pi/ardupilot/modules/waf/waf-light'
Download the ArduPilot code and update submodules:
  git clone https://github.com/ArduPilot/ardupilot.git
  cd ardupilot
  git pull
  git submodule update --init --recursive
Waf config
  waf configure --board=navio2
Build arducopter
  waf plane
Copy the binary
  cp build/navio2/bin/arduplane ~

## Slide 72: 나비오 PX4 설치(X)
필수 사항 아님.
PX4 소스 빌드
PX4 자동 실행 설정

## Slide 73: PX4 소스 빌드 1
문서
  https://docs.px4.io/en/flight_controller/raspberry_pi_navio2.html
Changing hostnames
Setting up Avahi (Zeroconf)
  sudo usermod -a -G dialout $USER
  sudo apt install avahi-daemon insserv -y
  sudo insserv avahi-daemon
  sudo apt install python-jinja2 -y
  sudo apt install cmake python-empy -y
  sudo apt install python-pip -y
  sudo pip install numpy toml pyyaml

## Slide 74: PX4 소스 빌드 2
빌드 유틸 다운로드
  wget https://raw.githubusercontent.com/PX4/Devguide/v1.9.0/build_scripts/ubuntu_sim_nuttx.sh
  source ./ubuntu_sim_nuttx.sh
폴더 이동
  cd ~/src/Firmware
소스 업데이트
  git pull
  git submodule sync --recursive
  git submodule update --init --recursive
빌드
  make emlid_navio2_native
실행
  cd ~/src/Firmware
  sudo killall arducopter
  sudo ./build/emlid_navio2_native/bin/px4 -s ./posix-configs/rpi/px4.config

## Slide 75: PX4 자동 실행 설정
sudo vi /etc/rc.local
  systemctl stop arducopter
  killall arducopter
  cd /home/pi/src/Firmware && ./build/emlid_navio2_native/bin/px4 -d -s ./posix-configs/rpi/px4.config > px4.log

## Slide 76: 영상 전송
비디오 장치 설정
GStream
MJPEG-Streamer
Raspivid

## Slide 77: Raspberry PI2 비디오 장치 설정
Enable camera options require a reboot to take effect.
  sudo raspi-config
비디오 장치 설정
  sudo modprobe bcm2835-v4l2
비디오 장치 확인
  ls /dev/video*
아래의 명령어로 카메라 정상 작동을 확인한다.
  raspistill –o cam.jpg

## Slide 78: Qground Video 사용 설정

## Slide 79: Gstream 동영상 서비스 방법
관제소프트웨어(QGroundControl 또는 MissionPlanner) 를 먼저 실행한다.
라즈베라파이에서 아래의 명령어를 실행한다. 아이피 주소를 노트북의 아이피 주소로 변경한다.
  raspivid -t 0 -fps 24 -b 2000000 -vf -hf -n -o - | gst-launch-1.0 -v fdsrc ! h264parse ! rtph264pay ! udpsink host=192.168.1.200 port=5600

## Slide 80: QGroundControl 동영상 저장
Video Stream 선택후에 Record Stream 버튼을 클릭한다.
동영상은 "Documents\QGroundControl\Video" 폴더에 저장된다.

## Slide 81: MissionPlanner 동영상 저장
동영상 조회 패널에서 마우스를 오른 쪽 클릭하여 Stop Recording / Start Recording 한다.
동영상은 "Documents\Mission Planner\logs" 폴더에 저장된다.

## Slide 82: Calibration
모터 테스트
Arming Check 설정

## Slide 83: APM Pre Arming Checks

## Slide 84: Compass 보정

## Slide 85: 배터리 설정 (Navio 추천 방법)

## Slide 86: 배터리 설정 (오지만 소장님 추천)

## Slide 87: Battery Failsafe 설정 (필수)

## Slide 88: Arming Check 설정
All 과 RC Channels 만을 미선택한다.
나머지는 모두 선택한다.
Write Params를 클릭한다.

## Slide 89: 모터 테스트 방법
모터 테스트는 RC 캘리브레이션을 먼저 수행하여야 가능하다.

## Slide 90: RC 사용 방법

## Slide 91: X8R Binding Procedure
Binding is the process of uniquely associating a particular receiver to a transmitter module. A transmitter module can be bound to multiple receivers (not to be used simultaneously). A receiver can only be bound to one transmitter module.
Follow the steps below to finish the binding procedure.
  Turn on the transmitter while holding the F/S button on the module (please refer to the module instruction manual for switch positions). Release the button. The RED LED on the XJT module will flash, indicating the transmitter is ready to bind to the receiver.
  Set X8R receiver in bind mode (see below chart for details), The RED LED on the receiver will flash, indicating the binding process is completed.
  Turn off both the transmitter and the receiver.
  Turn on the transmitter and connect the battery. The GREEN LED on the receiver indicates the receiver is receiving commands from the transmitter. The receiver/transmitter module binding will not have to be repeated, unless one of the two is replaced

## Slide 92: FrSky X8R 수신기 바인딩 1
바인딩 방법
  https://www.youtube.com/watch?v=RH_RuVbF2YU

## Slide 93: FrSky X8R 수신기 바인딩 2
바인딩 방법
  https://www.youtube.com/watch?v=jUkutJrzXFI

## Slide 94: FrSky X8R 수신기 바인딩

## Slide 95: FrSky X8R 수신기 바인딩

## Slide 96: X8R 수신기와 Navio 초기 연결
X8R 수신기와 Navio 초기 연결 모습
  바인딩 되지 않으면 수신기에 적색 LED가 깜빡 거림.

## Slide 97: X8R 수신기와 Navio 바인딩
X8R 수신기와 Navio 바인딩 결과
  바인딩 되지 않으면 수신기에 녹색 LED가 깜빡 거림.

## Slide 98: ArduPilot에서 RC 캘리브레이션
ArduPilot에서 RC 신호를 보정할 수 있음.

## Slide 99: FrSky RC -> Mission Planner Mapping
Mode 2
Action | Channel
Throttle | CH 3
Yaw | CH 4
Pitch | CH 2
Roll | CH 1

## Slide 100: FrSky RC -> Mission Planner Mapping

## Slide 101: RC Mode
Mode 1
Mode 2
“Mode 1” is the second most common control setup that people use.
“Mode 2” is by far the most common, especially in the United States.

## Slide 102: RC Stick Control

## Slide 103: RC Stick Control

## Slide 104: Stick Control : Air Plane

## Slide 105: Stick Control : Air Plane

## Slide 106: FrSKY X8R
공식적인 동작 범위는 2km

## Slide 107: FrSky Taranis 모드1/2 변경 방법

## Slide 108: RC 시동 방법
ardupilot RC 캘리브레이션에서 Mode2로 바인딩함.
Lower right the throttle lever for about 5 secs to arm.
Lower left the throttle lever for about 3 secs to disarm.

## Slide 109: NAVIO2 드론 조립 예
https://community.emlid.com/t/first-build-quadcopter-autonomous-drone-rpi-3-b-navio2/12597

## Slide 110: 부록

## Slide 111: PreArm 에러 해결책
logging failed

## Slide 112: PreArm: loggin failed
해결책
  https://community.emlid.com/t/navio2-prearm-logging-failed/14065
  There are two possibilities:
  SDcard log file is corrupted, I had the problem, sometimes with a fresh installation, sometimes after an uncontrolled crash like bad landing and fall on the side…
  Clearing the log list (delete the logs from the card) is a solution.
  Poor quality of the card. All class10 cards are not equal. I have some good results with Sandisk class10.
  I also use the close log after disarm option.

## Slide 113: LinuxPWM_Sysfs:Unable to open file /sys/class/pwm/pwmchip0/pwm0/duty_cycle
Please run
  sudo emlidtool rcio update -f
  without rebooting the RPi after that.

## Slide 114: PreArm: servo function 33 unassigned

## Slide 115: Command was denied by the autopilot

## Slide 116: Flight mode change failed

## Slide 117: PreArm: Check FS_THR_VALUE

## Slide 118: PreArm: Battery failsafe
http://ardupilot.org/copter/docs/failsafe-battery.html
The battery failsafe can be configured to automatically switch the vehicle into RTL, SmartRTL or Land mode if the vehicle battery voltage drops below a specified voltage for 10 seconds or the estimated remaining capacity has dropped below a configurable threshold.
When the failsafe will trigger
  voltage drops below the voltage held in the BATT_LOW_VOLT parameter (or FS_BATT_VOLTAGE in older versions) for more than 10 seconds. The default voltage is 10.5 volts. If set to zero the voltage based trigger will be disabled.
  remaining capacity falls below the BATT_LOW_MAH parameter (or FS_BATT_MAH in older versions) 20% of the battery’s full capacity is a good choice (i.e. “1000” for a 5000mAh battery). If set to zero the capacity based trigger will be disabled (i.e. only voltage will be used

## Slide 119: 공유기 설정

## Slide 120: 공유기 설정
Iptime 공유기나 TP-Link 공유기 매뉴얼 참고

## Slide 121: 호스트이름 변경

## Slide 122: 라즈베리파이 환경 설정 실행
sudo raspi-config
  A2 Hostname 선택

## Slide 123
Read the notice and click Ok:

## Slide 124
Enter the new hostname. The hostname should contain only letters, numbers, and the hyphen (-):
호스명은 navio_{영문이니셜3자}
변경후 라즈벨피 파이를 리부팅한다.

## Slide 125: 동영상 송수신
추천하지 않음.
실험시 필요에 따라 사용함.

## Slide 126: 영상 전송 방법
다음의 방법중 하나를 선택하여 영상을 전송한다.
  Gstream : 추천
  MJPG-Streamer
  Raspivid

## Slide 127: MJPEG-Streamer Install & Setup
https://github.com/cncjs/cncjs/wiki/Setup-Guide:-Raspberry-Pi-%7C-MJPEG-Streamer-Install-&-Setup-&-FFMpeg-Recording
  sudo apt-get install build-essential libjpeg8-dev imagemagick libv4l-dev cmake -y
  cd ~
  git clone https://github.com/jacksonliam/mjpg-streamer.git
  cd mjpg-streamer/mjpg-streamer-experimental
  make
  sudo make install
  ./start.sh

## Slide 128: MJPG 부팅시 자동 실행 설정
/etc/rc.local 파일에 아래 내용을 추가 한다.
  sudo vi /etc/rc.local
sudo modprobe bcm2835-v4l2
/usr/local/bin/mjpg_streamer -i "input_uvc.so -r 1280x720 -d /dev/video0 -f 30 -q 80" -o "output_http.so -p 80 -w /usr/local/share/mjpg-streamer/www" &
exit 0

## Slide 129: VLC 동영상 조회
Windows10에서 VLC media player를 설치한다.
Midia => Open Network Stream 클릭
  http://192.168.1.100:8080(HTTP TCP Port)/?action=stream

## Slide 130: 웹브라우저 동영상 조회
웹 브라우저에서 아래의 주소를 입력한다.
  http://<raspberry_ip_address>:<HTTP TCP port>/stream_simple.html
  예)http://192.168.1.201/stream_simple.html

## Slide 131: raspivid 를 이용한 동영상 서비스
On the PI:
  raspivid -t 0 -h 720 -w 1080 -fps 15 -b 2000000 -l -o tcp://0.0.0.0:3333
On the Computer, one can stream with VLC:
  vlc tcp/h264://192.168.66.154:3333
(assuming 192.168.66.154 is the PI's IP address)

## Slide 132: raspivid 사용법
Remember to use -hf and -vf to flip the image
  raspivid -o vid.h264
Capture 30 seconds of raw video at 640x480 and 150kB/s bit rate into a pivideo.h264 file:
  raspivid -t 30000 -w 640 -h 480 -fps 25 -b 1200000 -p 0,0,640,480 -o pivideo.h264
Wrap the raw video with an MP4 container:
  MP4Box -add pivideo.h264 pivideo.mp4
Remove the source raw file, leaving the remaining pivideo.mp4 file to play
  rm pivideo.h264
현재 시각으로 비디오 로그 남기는 방법
  raspivid -t 0 -h 720 -w 1080 -fps 15 -b 2000000 -o ~/video/`date +%F_%T`.h264

## Slide 133: 외부 장치 사용
외장 WiFi 사용법

## Slide 134: 외장 Wi-Fi 사용법
외장 Wi-Fi를 부착한다.
내장 Wi-Fi를 disable 시킨다.
  sudo ifconfig wlan0 down
내장 Wi-Fi를 다시 enable 하는 방법
  sudo ifconfig wlan0 down

## Slide 135: GPS 로그 분석
GPS 로그 전송 프로그램 설정
로그 분석 프로그램 u-center 설치

## Slide 136: GPS 데이터 전송 프로그램 설정
프로그램 다운로드 및 설치
  cd ~
  git clone https://github.com/sunabove/autopilot.git
  cd ~/autopilot/Utilities/ublox-spi-to-tcp
  make
  sudo cp ublox-spi-to-tcp /usr/bin

## Slide 137: GPS 데이터 전송 프로그램 자동 실행
부팅시 자동 실행 설정
  /etc/rc.local 파일에 맨 아랫중의 exit 0 줄 위에
  ublox-spi-to-tcp 5000 &
  을 추가한다.
파일 편집 명령어
  sudo nano /etc/rc.local
#!/bin/sh -e
#
# Print the IP address
_IP=$(hostname -I) || true
if [ "$_IP" ]; then
printf "My IP address is %s\n" "$_IP"
fi
ublox-spi-to-tcp 5000 &
exit 0

## Slide 138: 로그 분석 프로그램 u-center
u-center GPS 분석 프로그램 설치
  https://www.u-blox.com/en/product/u-center
  u-center for Windows 프로그램을 다운로드/설치

## Slide 139: u-center와 Navio2 GPS 연결
u-center 프로그램 실행
  Network connection 클릭
  Network connection 에 입력
    tcp://나비오 IP 주소:5000

## Slide 140: GPS 통계 분석
Statistic View 이 데이터를 복사하여 엑셀로 저장.

## Slide 141: GPS 데이터 분석 실험 자료 정리
같은 위치에서 실험을 한다.
실험 메터데이터 작성
  실험 일자/시간/장소/이름
  강우 확률/구름 분포 강도
프로그램 실행
  Mission Planner를 연결한다.
  u-center를 연결한다.
데이터 획득
  10분 정도 gps 데이터를 수신한다.
데이터 저장 / 실험시 마다 폴더별로 구분하여 파일을 저장.
  하늘 사진을 촬영하여 저장한다.
  u-center statistics view 자료를 복하사여 엑셀로 저장
  Mission Planner 전체 화면 캡쳐

## Slide 142: 용어 사전

## Slide 143: AHRS
Attitude Heading Reference Systems
  An attitude and heading reference system (AHRS) consists of sensors on three axes that provide attitude information for aircraft, including roll, pitch and yaw.
  These are sometimes referred to as MARG (Magnetic, Angular Rate, and Gravity) sensors and consist of either solid-state or microelectromechanical systems (MEMS) gyroscopes, accelerometers and magnetometers.
  They are designed to replace traditional mechanical gyroscopic flight instruments.
An AHRS is usually made up of the following LRUs.
  An attitude heading reference unit (AHRU)
  A flux valve or magnetometer
  A controller or panel-mounted switches
  A configuration module
https://helicoptermaintenancemagazine.com/article/layman%E2%80%99s-guide-attitude-heading-reference-systems-ahrs

## Slide 144: 용어 사전
HDOP: horizontal dilution of position

## Slide 145: 끝.