## Slide 1: NAVIO 2 드론 제작
2019년 6월 9일
성병문
한세대학교 자율 비행

## Slide 2: NAVIO 개요

## Slide 3: NAVIO2
홈페이지
  https://emlid.com/navio/
  https://docs.emlid.com/navio2/
What is NAVIO2?
  Autopilot HAT(Hardware Attached on Top) for Raspberry Pi
  Powered by ArduPilot and ROS
  Supports PX4
  $ 168
  Turn your Raspberry Pi® into a drone controller

## Slide 4: NAVIO2 특징
GNSS receiver
  Tracks GPS, GLONASS, Beidou, Galileo and SBAS satellites. External antenna with MCX connector
Dual IMU
  Accelerometers, gyroscopes and magnetometers for orientation and motion sensing
RC I/O co-processor
  Accepts PPM/SBUS input and provides 14 PWM output channels for motors and servos
High resolution barometer
  Senses altitude with 10 cm resolution
Extension ports
  Exposed ADC, I2C and UART interfaces for sensors and radios
Triple redundant power supply
  With overvoltage protection and power module port for voltage and current sensing

## Slide 5: NAVIO 운영체제 설치
This is a Raspbian you know with ArduPilot and ROS preinstalled and ready to run with a couple of simple commands. Also comes with DroneKit and GStreamer

## Slide 6: NAVIO H/W 조립
조립

## Slide 7: NAVIO2 드론 조립 예
https://community.emlid.com/t/first-build-quadcopter-autonomous-drone-rpi-3-b-navio2/12597
https://www.instructables.com/id/Step-by-step-Guidance-to-Build-a-Drone-From-Scratc/

## Slide 8: NAVIO2 조립
홈페이지
  https://docs.emlid.com/navio2/
Powering Navio2 Attention
  ALL POWER SOURCES SHOULD PROVIDE VOLTAGE IN 4.8-5.3V RANGE, OTHERWISE YOU CAN DAMAGE YOUR NAVIO2 AND RASPBERRY PI.**
Navio2 has three power sources, all of them can be used simultaneously as they are protected by ideal diodes.

## Slide 9: 나비오2 부품 설명

## Slide 10: 드론 Quadcopter NAVIO 조립

## Slide 11: Navio2 배선

## Slide 12: 파워 공급 1
Navio2 should be powered by a power module connected to the “POWER” port on Navio2.
Navio2 will provide power to the Raspberry Pi.

## Slide 13: 파워 공급 2

## Slide 14: GPS 연결

## Slide 15: ESC 연결
ESCs are connected to RC outputs labeled from 1 to 14 on a 2.54mm header.
Only one ESC power wire (central) should be connected to Navio2 servo rail, otherwise BECs built in ESCs will heat each other.

## Slide 16: 고도계 태양 광선 차단(필수)
MS5611 barometer (steel cap IC) is sensitive to UV light and might report sudden jumps in altitude under sunlight.
It is very important to cover it with a piece of open cell foam (something like microphone fabric) or put autopilot in a protective case to protect it both from sunlight and airstreams.

## Slide 17: RC input
Navio2는 PPM 과 SBUS 형식의 RC 신호만을 지원한다.
PPM 타입 RC Controller
  Frsky Taranis
    https://www.frsky-rc.com/product/taranis-x9d-plus-2/

## Slide 18: FrSKY X8R과 Navio2 연결 1

## Slide 19: FrSKY X8R과 Navio2 연결 2

## Slide 20: Telemetry Modem
UART radio
  For UART port use /dev/ttyAMA0 serial.

## Slide 21: Telemetry Modem
3DR 무선 텔레 메트리 433MHZ
  https://www.banggood.com/ko/New-Upgraded-V2_0-3DR-Radio-Telemetry-433MHZ-915MHZ-Data-Transmission-Module-For-APM-Pixhawk-PX4-p-1304758.html?ID=510651&cur_warehouse=CN

## Slide 22: Telemetry 연결 예시

## Slide 23: 진동 방지 받침대 1
We have designed an anti-vibration for Navio that can be easily 3D printed.
It significantly simplifies mounting and eliminates vibrations.

## Slide 24: 진동 방지 받침대 2
STL Files
  Top
    https://github.com/emlid/hardware/blob/master/VibroNavio2top_rev_A.STL
  Bottom
    https://github.com/emlid/hardware/blob/master/VibroNavio2bot_rev_A.STL
You will also need 8 blue vibration damping balls from Hobbyking
  https://hobbyking.com/en_us/vibration-damping-ball-65g-bag-of-8.html

## Slide 25: 라즈베리파이 케이스
https://www.thingiverse.com/thing:3712499?fbclid=IwAR0q23hTFudF2WR6drXF0MihutdcCVjp1nGQSJyXfh7dTh9L-Sk7-IEVzkE
https://www.thingiverse.com/thing:3714695?fbclid=IwAR2kpwI0rKJyGNhlsDpJ_Qi9enSqlocVV1SZ8qa6bXuRHgcDlFpWOtUVXCo

## Slide 26: NAVIO S/W
라즈비안 운영체제 설정
ardupilot 설정

## Slide 27: 라즈비안 운영체제 설정
라즈비안 운영체제 설치
라즈비안 환경 설정(Wi-Fi)
ardupilot 설정

## Slide 28: 나비오 S/W 설치
공식 문서
  https://docs.emlid.com/navio2/

## Slide 29: 라즈비안 설치
기설정된 라즈비안 이미지 다운로드
  http://files.emlid.com/images/emlid-raspbian-20190227.img.xz
Etcher를 이용하여 라즈비안 이미지를 SD-Card에 굽는다.
  Etcher 다운로드 : https://www.balena.io/etcher/

## Slide 30: 라즈비안 Wi-Fi 설정
Wi-Fi 설정
  sudo vi /etc/wpa_supplicant/wpa_supplicant.conf
    network={
      ssid="ADRONE"
      psk="12341234"
    }

## Slide 31: 라즈베리파이 IP 주소 알아내기
공유기에서 접속한 라즈베리파이의 아이피 주소를 알아낸다.

## Slide 32: 라즈베리파이 IP 주소 고정하기
공유기에서 접속한 라즈베리파이의 아이피 주소를 고정한다.

## Slide 33: 라즈베리파이 로그인
ssh 프로그램 다운로드
  bitvise ssh client 설치 :
    https://www.bitvise.com/download-area
라즈베리파이 로그인
  아이디: pi
  암호: raspberry

## Slide 34: 라즈비안 환경 설정 1
Hostname 변경
  navio_{영문이니셜 3자} 로 변경
  변경 방법
    https://geek-university.com/raspberry-pi/change-raspberry-pis-hostname/
root 파일 시스템 확장
  sudo raspi-config --expand-rootfs

## Slide 36: 라즈베리파이 환경 설정 2
암호 변경 : 암호를 a 로 변경한다.
  pi 사용자의 암호 변경
    sudo passwd pi
  관리자 암호 변경
    sudo passwd
업데이트/업그레이드는 일주일에 한 번 한다.
  sudo apt update
  sudo apt upgrade –y
  sudo apt autoremove

## Slide 37: 라즈베리 나비오 운영체제 정보
커널 버전 확인
  uname -a
배포판 버전 확인
  lsb_release -a

## Slide 38: Ardupilot 설치 사전 체크 사항

## Slide 39: SD Card 성능 벤처 마크

## Slide 40: SD Card 성능 체크
성능 체크 방법
  curl https://raw.githubusercontent.com/geerlingguy/raspberry-pi-dramble/master/setup/benchmarks/microsd-benchmarks.sh | sudo bash
  curl http://www.nmacleod.com/public/sdbench.sh | sudo bash

## Slide 41: Ardupilot 설정

## Slide 42: Ardupilot 설정
공식 문서
  https://docs.emlid.com/navio2/common/ardupilot/installation-and-running/

## Slide 43: Choosing a vehicle, version and board
To select the vehicle that would be launched by default you should configure it with emlidtool:
  sudo emlidtool ardupilot
Before configuration emlidtool checks your RCIO firmware and will suggest to update it if you have the outdated one:

## Slide 44: Choose your vehicle
In the example below we'll use arducopter but it could've been just as well arduplane or ardurover.

## Slide 45: Choose copter and Apply

## Slide 46: Specifying launching options
Open the file:
  sudo nano /etc/default/arducopter
  sudo systemctl daemon-reload
Here you can specify IP of your ground station.
TELEM1="-A udp:127.0.0.1:14550"
#TELEM2="-C /dev/ttyAMA0" # Options to pass to ArduPilot
ARDUPILOT_OPTS="$TELEM1 $TELEM2"
# -A is a console switch (usually this is a Wi-Fi link)
# -C is a telemetry switch
# Usually this is either /dev/ttyAMA0 - UART connector on your Navio
# or /dev/ttyUSB0 if you're using a serial to USB convertor
# -B or -E is used to specify non default GPS
접속 노트북의 IP 주소로 변경

## Slide 47: 최신 Ardupilot 프로그램 설치
나비오 설치 버전을 사용하거나
  cp /usr/bin/arducopter ~
최신 버전 다운로드 및 권한 부여
  wget --no-cache http://firmware.eu.ardupilot.org/Copter/stable/navio2/arducopter
  chmod +x arducopter

## Slide 48: Launching a custom ArduPilot binary 2
sudo nano /etc/systemd/system/ardupilot.service
[Unit]
Description=ArduPilot for Linux
After=systemd-modules-load.service
Documentation=https://docs.emlid.com/navio2/navio-ardupilot/installation-and-running/#autostarting-ardupilot-on-boot
Conflicts=arduplane.service arducopter.service ardurover.service
[Service]
EnvironmentFile=/etc/default/ardupilot
# Uncomment and modify this line if you want to launch your own binary
ExecStart=/bin/sh -c "/home/pi/arducopter -A udp:192.168.1.200:14550"
##### CAUTION ######
# There should be only one uncommented ExecStart in this file
Restart=on-failure
[Install]
WantedBy=multi-user.target
최신 ardupilot 프로그램 경로
접속 노트북의 IP 주소로 변경
Notes: sudo vi/etc/systemd/system/ardupilot.service

## Slide 49: Ardupilot 서비스 관리 3
ArduPilot 재시작
  sudo systemctl daemon-reload
  sudo systemctl status ardupilot
  sudo systemctl start ardupilot
  sudo systemctl enable ardupilot
라즈베리파이 리부팅
  sudo reboot
수동 실행 방법
  sudo arducopter -A udp:192.168.1.200:14550

## Slide 50: ardupilot 실행 확인 방법
아래의 명령어를 실행하여 ardupilot 실행 여부를 확인한다.
  ps -ef | grep ardu
비 정상 실행 상태 : 아이피 주소가 잘 못 됨.
정상 실행 상태 : 아이피 주소 확인

## Slide 51: Ardupilot 소스 빌드

## Slide 52: ardupilot 소스 빌드
Python 패키지 설치
  pip install future
Aliasing
  alias waf='/home/pi/ardupilot/modules/waf/waf-light'
Download the ArduPilot code and update submodules:
  git clone https://github.com/ArduPilot/ardupilot.git
  cd ardupilot
  git pull
  git submodule update --init --recursive
Waf config
  waf configure --board=navio2
Build arducopter
  waf copter
Copy the binary
  cp build/navio2/bin/arducopter ~

## Slide 53: 나비오 PX4 설치

## Slide 54: PX4 소스 빌드 1
문서
  https://docs.px4.io/en/flight_controller/raspberry_pi_navio2.html
Changing hostnames
Setting up Avahi (Zeroconf)
  sudo usermod -a -G dialout $USER
  sudo apt install avahi-daemon insserv
  sudo insserv avahi-daemon
  sudo apt install python-jinja2
  sudo apt install cmake python-empy
  sudo pip install numpy toml

## Slide 55: PX4 소스 빌드 2
빌드 유틸 다운로드
  wget https://raw.githubusercontent.com/PX4/Devguide/v1.9.0/build_scripts/ubuntu_sim_nuttx.sh
  source ./ubuntu_sim_nuttx.sh
폴더 이동
  cd ~/src/Firmware
소스 업데이트
  git pull
  git submodule sync --recursive
  git submodule update --init --recursive
빌드
  make emlid_navio2_native
실행
  sudo killall arducopter
  sudo ./build/emlid_navio2_native/bin/px4 -s ./posix-configs/rpi/px4.config

## Slide 56: PX4 자동 실행
sudo vi /etc/rc.local
  systemctl stop arducopter
  killall arducopter
  cd /home/pi/src/Firmware && ./build/emlid_navio2_native/bin/px4 -d -s ./posix-configs/rpi/px4.config > px4.log

## Slide 57: Video Streaming

## Slide 58: Raspberry PI2 비디오 장치 설정
Enable camera options require a reboot to take effect.
  sudo raspi-config
비디오 장치 설정
  sudo modprobe bcm2835-v4l2
비디오 장치 확인
  ls /dev/vidio*
아래의 명령어로 카메라 정상 작동을 확인한다.
  raspistill –o cam.jpg

## Slide 59: MJPEG-Streamer Install & Setup
https://github.com/cncjs/cncjs/wiki/Setup-Guide:-Raspberry-Pi-%7C-MJPEG-Streamer-Install-&-Setup-&-FFMpeg-Recording
  sudo apt-get install build-essential libjpeg8-dev imagemagick libv4l-dev cmake -y
  cd ~
  git clone https://github.com/jacksonliam/mjpg-streamer.git
  cd mjpg-streamer/mjpg-streamer-experimental
  make
  sudo make install
  ./start.sh

## Slide 60: 라즈베리파이 부팅시 자동 실행 설정
/etc/rc.local 파일에 아래 내용을 추가 한다.
  sudo vi /etc/rc.local
sudo modprobe bcm2835-v4l2
/usr/local/bin/mjpg_streamer -i "input_uvc.so -r 1280x720 -d /dev/video0 -f 30 -q 80" -o "output_http.so -p 80 -w /usr/local/share/mjpg-streamer/www" &
exit 0

## Slide 61: 동영상 조회
웹 브라우저에서 아래의 주소를 입력한다.
  http://<raspberry_ip_address>/stream_simple.html
  http://192.168.1.201/stream_simple.html

## Slide 62: Calibration
모터 테스트
Arming Check 설정

## Slide 63: APM Pre Arming Checks

## Slide 64: 모터 테스트 방법
모터 테스트는 RC 캘리브레이션을 먼저 수행하여야 가능하다.

## Slide 65: Arming Check 설정
All 과 RC Channels 만을 미선택한다.
나머지는 모두 선택한다.
Write Params를 클릭한다.

## Slide 66: 배터리 설정

## Slide 67: RC 사용 방법

## Slide 68: X8R Binding Procedure
Binding is the process of uniquely associating a particular receiver to a transmitter module. A transmitter module can be bound to multiple receivers (not to be used simultaneously). A receiver can only be bound to one transmitter module.
Follow the steps below to finish the binding procedure.
  Turn on the transmitter while holding the F/S button on the module (please refer to the module instruction manual for switch positions). Release the button. The RED LED on the XJT module will flash, indicating the transmitter is ready to bind to the receiver.
  Set X8R receiver in bind mode (see below chart for details), The RED LED on the receiver will flash, indicating the binding process is completed.
  Turn off both the transmitter and the receiver.
  Turn on the transmitter and connect the battery. The GREEN LED on the receiver indicates the receiver is receiving commands from the transmitter. The receiver/transmitter module binding will not have to be repeated, unless one of the two is replaced

## Slide 69: FrSky X8R 수신기 바인딩 1
바인딩 방법
  https://www.youtube.com/watch?v=RH_RuVbF2YU

## Slide 70: FrSky X8R 수신기 바인딩 2
바인딩 방법
  https://www.youtube.com/watch?v=jUkutJrzXFI

## Slide 71: X8R 수신기와 Navio 초기 연결
X8R 수신기와 Navio 초기 연결 모습
  바인딩 되지 않으면 수신기에 적색 LED가 깜빡 거림.

## Slide 72: X8R 수신기와 Navio 바인딩
X8R 수신기와 Navio 바인딩 결과
  바인딩 되지 않으면 수신기에 녹색 LED가 깜빡 거림.

## Slide 73: ArduPilot에서 RC 캘리브레이션
ArduPilot에서 RC 신호를 보정할 수 있음.

## Slide 74: RC Mode
Mode 1
Mode 2
“Mode 1” is the second most common control setup that people use.
“Mode 2” is by far the most common, especially in the United States.

## Slide 75: FrSKY X8R
공식적인 동작 범위는 2km

## Slide 76: FrSky Taranis 모드1/2 변경 방법

## Slide 77: RC 시동 방법
ardupilot RC 캘리브레이션에서 Mode2로 바인딩함.
Lower right the throttle lever for about 5 secs to arm.
Lower left the throttle lever for about 3 secs to disarm.

## Slide 78: NAVIO2 드론 조립 예
https://community.emlid.com/t/first-build-quadcopter-autonomous-drone-rpi-3-b-navio2/12597

## Slide 79: 부록

## Slide 80: PreArm 에러 해결책
logging failed

## Slide 81: PreArm: loggin failed
해결책
  https://community.emlid.com/t/navio2-prearm-logging-failed/14065
  There are two possibilities:
  SDcard log file is corrupted, I had the problem, sometimes with a fresh installation, sometimes after an uncontrolled crash like bad landing and fall on the side…
  Clearing the log list (delete the logs from the card) is a solution.
  Poor quality of the card. All class10 cards are not equal. I have some good results with Sandisk class10.
  I also use the close log after disarm option.

## Slide 82: LinuxPWM_Sysfs:Unable to open file /sys/class/pwm/pwmchip0/pwm0/duty_cycle
Please run
  sudo emlidtool rcio update -f
  without rebooting the RPi after that.

## Slide 83: 공유기 설정

## Slide 84: 공유기 설정
Iptime 공유기나 TP-Link 공유기 매뉴얼 참고

## Slide 85: 호스트이름 변경

## Slide 86: 라즈베리파이 환경 설정 실행
sudo raspi-config
  A2 Hostname 선택

## Slide 87
Read the notice and click Ok:

## Slide 88
Enter the new hostname. The hostname should contain only letters, numbers, and the hyphen (-):
호스명은 navio_{영문이니셜3자}
변경후 라즈벨피 파이를 리부팅한다.

## Slide 89: 용어 사전

## Slide 90: 용어 사전
HDOP: horizontal dilution of position

## Slide 91: 끝.